## Slide 1
The Probability Model
Algebra of events
Probability and conditional probability.
Applications
- Network reliability
- Binary communication
- Information and coding

## Slide 2
Sample Space and Events
A2
A1
● s
events
S

## Slide 3
Events and Event Operations
  S Certain event
  0 Null event
  A1, A2, A3,… User defined events
  A1 + A2 Union operation (A1  A2)
  A1 A2 Intersection operation (A1  A2)
  AC Complement operation
  S Certain event
  0 Null event
  A1, A2, A3,… User defined events
  A1 + A2 Union operation (A1  A2)
  A1 A2 Intersection operation (A1  A2)
  AC Complement operation

## Slide 4
Example:
Consider a sample space represented by S = {1,2,3,4,5,6}
Let A1 = {1,3,5}, A2 = {1,2}, and A3 = {2,4,6} be user-defined events.
Find:
  A1C
  A2 + A3
  A1 + A3
  A1 A2
  A1 A3
  A1 + 0
  A1 0
A1=
{1, 3, 5}
A1C =
{2, 4, 6}
S = {1,2,3,4,5,6}
= ({1,3,5})C
= {1,2,4,6}
= {1,2,3,4,5,6} = S
= {1}
= 0
= {1,3,5} = A1
= {2,4,6}
  = A3

## Slide 5
Example:
Consider a sample space represented by S = {1,2,3,4,5,6}
Let A1 = {1,3,5}, A2 = {1,2}, and A3 = {2,4,6} be user-defined events.
Find:
  A1C
  A2 + A3
  A1 + A3
  A1 A2
  A1 A3
  A1 + 0
  A1 0
A1=
{1, 3, 5}
A1C =
{2, 4, 6}
S = {1,2,3,4,5,6}
= ({1,3,5})C
= {1,2,4,6}
= {1,2,3,4,5,6} = S
= {1}
= 0
= {1,3,5} = A1
= 0
= {2,4,6}
  = A3

## Slide 6
Axioms for the Algebra of Events
A1A1C = 0 Mutual exclusion
A1S = A1 Inclusion
(A1C)C = A1 Double complement
A1 + A2 = A2 + A1 Commutative law
A1 + (A2 + A3) = (A1 + A2) + A3 Associative law
A1(A2 + A3) = A1A2 + A1A3 Distributive law
(A1A2) C = A1C + A2C De Morgan’s law
A1A1C = 0 Mutual exclusion
A1S = A1 Inclusion
(A1C)C = A1 Double complement
A1 + A2 = A2 + A1 Commutative law
A1 + (A2 + A3) = (A1 + A2) + A3 Associative law
A1(A2 + A3) = A1A2 + A1A3 Distributive law
(A1A2) C = A1C + A2C De Morgan’s law

## Slide 7
Additional Identities
SC = 0
A1 + 0 = A1 Inclusion
A1A2 = A2A1 Commutative law
A1(A2A3) = (A1A2)A3 Associative law
A1 + (A2A3) = (A1 + A2) (A1 + A3) Distributive law
(A1 + A2)C = A1CA2C De Morgan’s law
SC = 0
A1 + 0 = A1 Inclusion
A1A2 = A2A1 Commutative law
A1(A2A3) = (A1A2)A3 Associative law
A1 + (A2A3) = (A1 + A2) (A1 + A3) Distributive law
(A1 + A2)C = A1CA2C De Morgan’s law

## Slide 8
Finite Unions and Intersections
These are included in the algebra.
Infinite Unions and Intersections
If they are included, the algebra of events is called a Sigma Algebra.
∞
∞

## Slide 9
Mutually Exclusive and Collectively Exhaustive Events
Mutually exclusive:
Collectively exhaustive:
A set of events that is mutually exclusive and collectively exhaustive is called a partition.
Working Definition of the Sample Space
THE SAMPLE SPACE IS REPRESENTED BY THE FINEST
GRAIN, MUTUALLY EXCLUSIVE, COLLECTIVELY
EXHAUSTIVE SET OF OUTCOMES FOR AN EXPERIMENT.

## Slide 10
Discrete Sample Space
Discrete sample space <=> Discrete valued signals
Output of an 8-bit ADC contains only 28 = 256 values S = {-5, -4.9609375, …, -0.0390625,0,0.0390625, …, 4.9609375}
or S = {-128, -127, …, -1, 0, 1, …, 127}
(decimal equivalent of 2’s complement representation)
Discrete sample space has a finite or countably infinite number of outcomes.
  – In this example we have 256 outcomes (finite).
8-bit
ADC
s(t)
5V to +5V
s[n]

## Slide 11
Continuous Sample Space
Continuous sample space <=> Continuous magnitude signals
Output of the radio receiver is measured at t = t1. The dynamic range of the receiver output is -5V to +5V
  S = {s: -5  s  +5}
A continuous sample space has uncountably infinite values or outcomes
  – s could take values like 4.9326784531432677…
Examples of events and probability assignments:
Radio
Receiver
5V to +5V
s(t)

## Slide 12
2
2
1
3
4
5
6
1
3
4
5
6
Two Dimensional Sample Space
Roll two dice [discrete sample space]
  S = {(i,j): (1,1), (1,2), (1,3), …, (4,3), …, (6,4), (6,5), (6,6)}
Roll 4
Roll Doubles
Roll 10 or more

## Slide 13
Axioms of Probability
A1
A2

## Slide 14
Some Corollaries
A1
A2
A2
A1

## Slide 15
Pr[B] = Pr[BA1] + Pr[BA2] + … + Pr[BAn]
Pr[B] = Pr[BA1] + Pr[BA2] + … + Pr[BAn]
A2
An
B
The Principle of Total Probability
Let A1, A2, …, An be a set of mutually exclusive and collectively
exhaustive events:
then
Now let B be any event in S. Then,
A1
Pr[BA1]
+ Pr[BA2]

## Slide 16
Independence of Events
Two events A1 and A2 are said to be statistically independent
if and only if
Pr[A1A2] = Pr[A1] Pr[A2]
When the situation claims that events are “independent,”
this is the one and only test.

## Slide 17
System Reliability Calculations
Series connection of switches
Assume that switch failures are independent; and failure
results in an open connection.
F = {no connection between x and y} = A1+ A2
The probability that the connection fails: Pr[F] = Pr[A1+ A2] = Pr[A1] + Pr[A2] - Pr[A1A2]
= Pr[A1] + Pr[A2] - Pr[A1] Pr[A2] (A1 and A2 are independent)
= p + p - p2 = 2p - p2
S1
S2
y
x

## Slide 18
System Reliability Calculations
Parallel Connection of switches
Define: A1 = {S1 fails}, Pr[A1] = p, Pr[A1c] = 1 - p = q
A2 = {S2 fails}, Pr[A2] = p, Pr[A2c] = 1 - p = q
F = {no connection between x and y} = A1A2
The probability that the connection fails: Pr[F] = Pr[A1A2] = Pr[A1] Pr[A2] = p2 (A1 and A2 are independent)
S1
S2
y
x

## Slide 19
Combination Example
Consider a simple switching network as follows:
Define: Ak = {switch Sk is open}, k = 1,2,3,4 Pr[Ak] = p
Let F = {no connection between x and y} = (A1 + A2)A3 + A4
S1
S2
S3
S4
x
y

## Slide 20
(a) Find the probability that the path between x and y is established.
The probability of path failure is given by
→ Pr[F] = Pr[(A1 + A2)A3 + A4]
= Pr[A1A3 + A2A3] + Pr[A4] - Pr[A1A3A4 + A2A3A4]
= Pr[A4] + Pr[A1A3] + Pr[A2A3] - Pr[A1A2A3]
- Pr[A1A3A4] - Pr[A2A3A4] + Pr[A1A2A3A4]
= p + p2 + p2 - p3 - p3 - p3 + p4
= p + 2p2 - 3p3 + p4
= Pr[A1A3 + A2A3] + Pr[A4] - Pr[A1A3A4 + A2A3A4]
= Pr[A4] + Pr[A1A3] + Pr[A2A3] - Pr[A1A2A3]
- Pr[A1A3A4] - Pr[A2A3A4] + Pr[A1A2A3A4]
S1
S2
S3
S4
x
y
= Pr[(A1A3 + A2A3) + A4]
= Pr[A1A3 + A2A3] + Pr[A4] - Pr[A1A3A4 + A2A3A4]
= Pr[A4] + Pr[A1A3] + Pr[A2A3] - Pr[A1A2A3]
Combination Example (cont’d)

## Slide 21
(a) Find the probability that the path between x and y is established.
The probability of path failure is given by
→ Pr[F] = Pr[(A1 + A2)A3 + A4]
= Pr[A1A3 + A2A3] + Pr[A4] - Pr[A1A3A4 + A2A3A4]
= Pr[A4] + Pr[A1A3] + Pr[A2A3] - Pr[A1A2A3]
- Pr[A1A3A4] - Pr[A2A3A4] + Pr[A1A2A3A4]
= p + p2 + p2 - p3 - p3 - p3 + p4
= p + 2p2 - 3p3 + p4
The desired probability is then given by
Pr[path established] = 1 - Pr[F] = 1 - p - 2p2 + 3p3 - p4
S1
S2
S3
S4
x
y
= Pr[(A1A3 + A2A3) + A4]
Combination Example (cont’d)

## Slide 22
Probability as a function of parameter ‘p’
p 1 - Pr[F]
0.1 0.88290000
0.01 0.98980299
0.001 0.99899800
0.0001 0.99989998
Pr[path established] = 1 - Pr[F] = 1 - p - 2p2 + 3p3 - p4

## Slide 23
Repeated Independent Trials (Bernoulli Trials)
A random experiment, E, consists of several sub-experiments
or trials, Ei:
  All sub-experiments have the same sample space, Si.
  Events from all sub-experiments are mutually independent:
  Pr[A1A2A3...An] = Pr[A1]Pr[A2]Pr[A3]...Pr[An],
  where Ai is an event from Si.
  The sample space of E is:
    S = S1  S2  S3  ...  Sn
  All sub-experiments have the same sample space, Si.
  Events from all sub-experiments are mutually independent:
  Pr[A1A2A3...An] = Pr[A1]Pr[A2]Pr[A3]...Pr[An],
  where Ai is an event from Si.
  The sample space of E is:
    S = S1  S2  S3  ...  Sn

## Slide 24
A sequence of 4 bits is transmitted over a channel. Bit errors occur with probability 0.05. What is the sample space and what are the probabilities of the outcomes?
For a single bit we have 2 sub-events:
Φ no error Pr[Φ] = 0.95
E error Pr[E] = 0.05
The sample space and probabilities are:
Example of Bernoulli Trials
ΦΦΦΦ | ΦΦΦE | ΦΦEΦ | ΦΦEE | … | EEEE
(0.95)4 | (0.95)3(0.05) | (0.95)2(0.05)(0.95) | (0.95)2(0.05)2 | … | (0.05)4
0.8145 | 0.0429 | 0.0429 | 0.0023 | … | 6.25E-6

## Slide 25
Counting Methods and Probabillity
The assignment of probability is given by
The rule of products:
Consider an experiment with n outcomes; repeat it r times
The total number of outcomes is given by
or in the general case

## Slide 26
Examples
Roll a die 4 times sequentially. The total number of outcomes is
Form 5-letter words using 26 English alphabet characters. Characters can be repeated, and the words so formed do not have to be meaningful.
Construct variable names of length 3 using a letter, a number, and a letter (e.g., A2C).

## Slide 27
Permutations
(products without replacement)
Select r objects from among a given set of n distinct objects
where we pay attention to the order in which the r objects
are selected.
Important special case:
For r = n:

## Slide 28
Permutation Example
Form 5-letter words using the English alphabet. The characters
cannot be repeated, and the words do not have to be meaningful.
The total number of words that can be formed is:

## Slide 29
Combinations
Select r objects from among a given set of n distinct objects
where we pay no attention to the order in which the r objects
are selected.
Binomial coefficient “n choose r”

## Slide 30
Permutations and Combinations Example
Consider 5 workstations having equal capabilities: {a, b, c, d, e}
Permutations: Select two workstations where one will be a server and the other a graphics workstation. The possible selections are:
  ab ba ac ca ad da ae ea bc cb bd db be eb cd dc ce ec de ed
Combinations: Select two workstations where both will be used as graphics workstations. The possible selections are:
  ab ac ad ae bc bd be cd ce de
“ab  ba”
“ab = ba”

## Slide 31
Buying Computers
We plan to buy 5 personal computers. The computer store has a stock of 10 foreign-made PCs and 15 US-made PCs that meet our specifications.
(a) Assuming that the 5 computers are randomly chosen from this lot, what is the probability that exactly 3 US-made computers are selected?
  The sample space is given by
    S = {combinations of r = 5 chosen from n = 25}
  The desired event A = {exactly 3 of the 5 selected are US-made}

## Slide 32
Buying Computers (cont’d)
  The probability that we have 3 US-made computers is
[Hyper geometric distribution]

## Slide 33
Buying Computers (cont’d)
(b) Assuming that the 5 computers are randomly chosen from this lot, what is the probability that at least 1 is foreign made?
  The desired event B = {one or more of the 5 are foreign made}
  Let event C = {none of the 5 selected computers is foreign-made}
  Since B = CC, we can write Pr[B] = 1 - Pr[C]

## Slide 34
Another Example
Consider a box of 25 modem chips; 5 of them are known to be defective.
Select 6 from the box at random and test them. What is the probability that exactly 2 are defective?
  Sample Space: S = {combinations of r = 6 chosen from n = 25}
  Event: A = {exactly 2 of the 6 selected chips are defective}
  The number of outcomes in S is given by:
  For the selected 6 chips, we are interested in the case, where 2 are defective (i.e., they are from the 5 defective chips in the box) and 4 are non-defective (i.e., they are from the 20 non-defective chips in the box).

## Slide 35
Example (cont’d)
  The number of outcomes in A is given by:
  The probability that exactly 2 of the 6 selected chips are defective is

## Slide 36
Conditional Probability
Probability of occurrence of one event (say, A1) subject to the
knowledge that another event (say, A2) has occurred.
Pr[A1 | A2] is read as “probability of A1 given A2 ”
If A1 and A2 are independent, then
A1
A2
S

## Slide 37
Conditional Probability Example
Consider a sequence of 3 binary numbers (occurring randomly).
Sample space: S = {000, 001, 010, 011, 100, 101, 110, 111}
Find the probability of more 1’s than 0’s given the first bit is a 1.
Define two events:
  A1 = {more 1’s than 0’s} = {011, 101, 110, 111} (0.5)
  A2 = {the first bit is a 1} = {100, 101, 110, 111} (0.5)
Their intersection:
  A1A2 = {101, 110, 111} (0.375)

## Slide 38
Event Tree Used to Form a Sample Space
A
Ac
A B
A Bc
Ac B
Ac Bc
Pr[A]
Pr[Bc|A]
Pr[ABc] = Pr[Bc|A] Pr[A]
Pr[B|A]
Pr[Ac]
Pr[B|Ac]
Pr[Bc|Ac]

## Slide 39
Computation of Probabilities
F
Fc
F R
F Rc
Fc R
Fc Rc
1/5
0.25
4/5
0.75
0.15
0.85
(1/5)(0.75)
(1/5)(0.25)
(4/5)(0.15)
(4/5)(0.85)
Sample
Space Probability

## Slide 40
0
0
1
1
1
0.5
0.5
0
0
1
0
0
0.5
0.5
0.5
0.5
1
1
1
0
0
0
Sample
Space Probability
111 0.125
110 0.125
101 0.125
100 0.125
011 0.125
010 0.125
001 0.125
000 0.125
Event A1 =
{more 1’s than 0’s}
110
101
100
011
1
Event A2 =
{the first bit is a 1}
All 8 events in the sample space have probability 1/8, therefore
The conditional probability is obtained as follows:
Tree diagram
Example (cont’d)
100
111
A1A2
1
1

## Slide 41
Principle of Total Probability Revisited
Let A1, A2, …, An be mutually exclusive and collectively
exhaustive events. Let B be an event in S.
Then,
A2
An
B
BA2
A1

## Slide 42
Binary Communication Channel
Channel
1S
Transmitter
Receiver
Pr[0R|0S] = 0.95
0S
0R
1R
Pr[1R|1S] = 0.90
Pr[1R| 0S] = 0.05
Pr[0R|1S] = 0.10
Pr[0S] = 0.5
Pr[1S] = 0.5
0
0
1
1
We can compute the probability of joint events:
Pr[0S0R] = Pr[0R|0S]Pr[0S] = (0.95)(0.5) = 0.475
Pr[0S1R] = Pr[1R|0S]Pr[0S] = (0.05)(0.5) = 0.025 (error)

## Slide 43
Binary Communication Channel (cont’d)
Computing the probability of error:
Probability
0.050
0.450
0.025
0.475
0.5
0.10
1S0R
(error)
0S0R
0S1R
(error)
1S1R
1R
0.5
0S
0.95
0R
0.05
1S
0R
1R
conditional
a priori
0.90
0.5
0.10
0.050
0.5
0.05
0.025
Pr[error] = 0.050 + 0.025 = 0.075

## Slide 44
1S
0S
error
Use the Law of Total Probability:
Binary Communication Channel (cont’d)
Compute the probability of error another way:

## Slide 45
More on Conditional Probability
From the definition of conditional probability, we can write
This can be written as

## Slide 46
Let A1, A2, …, An be a set of mutually exclusive, collective
exhaustive events (partition). Then,
Or, applying the Principle of Total Probability
This is called Bayes’ Rule.
Bayes’ Rule

## Slide 47
Binary Communication Channel Revisited
Transmitter
Receiver
Pr[0R|0S] = 0.95
0
0
1
Pr[1R|1S] = 0.90
Pr[1R| 0S] = 0.05
Pr[0R|1S] = 0.10
Pr[0S] = 0.5
Pr[1S] = 0.5
Determine the inverse probability, P[1S |1R].

## Slide 48
Determine the inverse probability, P[1S |1R]:
Binary Communication Channel (cont’d)

## Slide 49
Integrated Circuit Example
Consider 3 boxes of integrated circuits (ICs).
Box 1 contains 1500 ICs and 10% of them are defective;
Box 2 contains 2000 ICs and 20% of them are defective; and
Box 3 contains 3000 ICs and 16% of them are defective.
Select 1 of the 3 boxes at random and choose an IC from
that box at random.

## Slide 50
By the principle of total probability, we can write
Define: A = “selected IC is defective” ,
Bi = “IC is from box i”
B1
B3
A
B2
(a) What is the probability that this IC is defective?
Integrated Circuit Example (cont’d)

## Slide 51
(b) Suppose that the selected IC is found to be defective.
What is the probability that this IC came from box #3?
By Bayes’ theorem, we can write
(c) Suppose all IC’s are mixed in one box and an IC is selected
at random. What is the probability that the IC is defective?
Integrated Circuit Example (cont’d)

## Slide 52
Basic Information Theory
Given an event A and its probability Pr[A], the “information” associated with A is defined by
where x is the base of the logarithm:
if x = 2, the units of information are bits;
if x = 10, the units are hartleys;
and if x = e, the units are nats.
Note the identity: loga b = x means that ax = b.

## Slide 53
Information Theory Example Consider two events: A1 and A2 with corresponding probabilities of occurrence of 0.125 and 0.875, respectively.
  The information associated with these events:
  I[A1] = -log2 (0.125) = 3 bits
  I[A2] = -log2 (0.875) = 0.1925 bits

## Slide 54
Entropy
Given a set of independent events that are mutually exclusive and collectively exhaustive, the average information associated with the random experiment is defined as

## Slide 55
Entropy Example Consider a sequence 1 2 3 2 3 4 5 4 5 6 7 8 9 8 9 0.
We estimate the probability of occurrence of each symbol as follows:
Pr[1] = Pr[6] = Pr[7] = Pr[0] = 1/16
Pr[2] = Pr[3] = Pr[4] = Pr[5] = Pr[8] = Pr[9] = 2/16
  The entropy of this sequence is

## Slide 56
Shannon-Fano Code
Messages are composed of an alphabet in which the frequency of occurrence of each letter is a probabilistic phenomenon.
  – For transmission purposes the messages are compressed such that the code length of a letter is inversely proportional to its frequency of occurrence (e.g., think of the Morse code).
  – Since the letters are transmitted sequentially, no short codeword can be part of the start of a longer codeword for unique decodability.
Shannon-Fano Algorithm:
  – Arrange letters in a descending order of their probabilities by breaking any ties arbitrarily.
  – Starting at the top, partition the letters into two equi-probable subgroups (as closely as possible): assign 0 to the first subgroup and 1 to the second.
  – Continue partitioning the subgroups until all letters are exhausted: after each partition, assign a 0 to the first group and a 1 to the second and append the newly assigned bits to the previously assigned bits.

## Slide 57
Example
Given a text message “ELECTRICAL ENGINEERING,” determine the relative probabilities of the letters in the message and find the Shannon- Fano code for each letter. Ignore the space character.
Since there are 21 letters in the message, we have the following probabilities:
Letters: {E, L, C, T, R, I, A, N, G}
Probabilities: {5/21, 2/21, 2/21, 1/21, 2/21, 3/21, 1/21, 3/21, 2/21}
Code assignment:
  E 5/21
  I 3/21
  N 3/21
  L 2/21
  C 2/21
  R 2/21
  G 2/21
  T 1/21
  A 1/21
Codeword Length
00 2
010 3
011 3
100 3
1010 4
1011 4
110 3
1110 4
1111 4