## Slide 1: Chapter 2 Computer Imaging Systems

## Slide 2: Imaging Systems Overview
Consists of two primary component types:
Hardware – Image acquisition system, computer, and display devices
Software – Image manipulation, analysis, and processing

## Slide 3: Imaging System Hardware
Notes: Fig 2.1-1

## Slide 4
Digital Camera Interfaces
 | 10 Gigabit Ethernet (IEEE 802.3-2015) | Firewire S3200 (IEEE 1394) | USB 3.1 | Camera Link
Type of standard | Public | Public | Public | Commercial
Connection Type | Point-to-point or Local Area Network (LAN) | Peer-to-peer, shared bus | Master-slave, shared bus | Point-to-point
Maximum Bandwidth for Images | ~10.0 Gigabit/sec (Gbs) | ~3.2 Gbs | ~10 Gbs | ~2.0 to 7.0 Gbs
Distance | ~100 meters, no limit with switches or fiber | ~4.5 meters, ~72 meters with switches, ~200 meters with fiber | ~5 meters, ~30 meters with switches | ~10 meters
PC Interface | Network | PCI card | PCI card | PCI frame grabber
Wireless support | Yes | No | No | No
Max # of Devices | Unlimited | 63 | 127 | 1
Notes: Table 2.1

## Slide 5
Analog Video Signal
Voltage
Time

## Slide 6
Digitization: transformation of video signal into digital image
Digitizing (sampling) an analog video signal

## Slide 7: Digital Video
Digital television (DTV) – standard definition TV (SDTV) and high definition (HDTV)
SDTV similar to previous analog, NTSC, SECAM, PAL
HDTV standards: 1280 columns by 720 rows (lines), in progressive scan mode, referred to as 720p, or 1920x1080 in interlaced mode, called 1080i
SDTV uses a 4:3 aspect ratio, the newer HDTV standards specifies a 16:9 aspect ratio

## Slide 9
Image is accessed as a 2-D array of data, where each data point is referred to as a pixel
Notation:
I(r,c) = Brightness of image at the pt (r,c)
where
r = row, and c = column

## Slide 10: The Hierarchical Image Pyramid

## Slide 11: Image Formation and Sensing

## Slide 12
Key components of image formation
Where will the image point appear?
  Determined by lenses and the physics of light,
  the science of optics
Value, or brightness, of that point?
  Sensor and electronic technology

## Slide 13: Visible Light Imaging
Reflectance function determines manner in which objects reflect light
Notes: Fig 2.2-2

## Slide 14: The Reflectance Function
Reflectance function determines an object’s appearance
Texture by light scattering and color by wavelengths reflected and absorbed
Notes: Fig 2.2-3

## Slide 15
Brightness:
Irradiance (Image brightness): Amount of light falling on surface, measured by a sensor
Irradiance = Power / Area
Radiance (Scene brightness): Amount of light emitted from a surface into a unit solid angle
Radiance = Power/(Area * Solid Angle)
Notes: Fig 2.2-4

## Slide 16
Lens equation: 1/a + 1/b = 1/f
f is the focal length and is an intrinsic property of the lens
Notes: Fig 2.2-5

## Slide 17
Blur equation: c = (d/b’)|b’ – b|
Notes: Fig 2.2-6

## Slide 18
Depth of field (Depth of focus): Range of distances over which objects are focused sufficiently well (blur circle equal or smaller than device resolution)
Depth of field can be controlled by adjusting the diaphragm
f-number (f-stop): Ratio of the focal length to the lens diameter
Depth of field is directly proportional to f-number

## Slide 19
Field of view (FOV) : Angle of cone of directions from which the device will create the image
FOV = 2Ø, where Ø = tan­-1( (d/2)/f)
Depends upon focal length of the lens and size of image sensor
f
d
φ
Lens
Image Sensor

## Slide 20
Types of Lenses:
  Wide Angle lens: Short focal length,
  FOV greater than 45°
  Normal lens: Medium focal length,
  FOV from 25° to 45°
  Telephoto lens: Long focal length,
  FOV less than 25°
Real lens consists of multiple lenses, as single lens may contain aberrations

## Slide 21
Vignetting effect:
  Negative effects of compound lens
  Decreases the amount of energy to the image plane passing through the lens, as we move farther away from the center of the lens
  Can be avoided by using center portion of the lens
Image Sensor

## Slide 22
Sensors : Converts light energy into electrical energy
a) Single imaging sensor ; b) Linear ( line) sensor ; c) 2-D or array sensor
CCD: 9kx9k CMOS: less power, cheaper, image quality not as good as CCD

## Slide 23
Sensor equation: Calculates the approximate number of electrons (N) liberated in a sensor
  N = δAδt∫ b(λ)q(λ)dλ
  δA is the area; δt is the time interval
  q(λ) is the quantum efficiency – the ratio of electron flux produced to the incident photon flux
  b(λ) is incident photon flux (irradiation)
Tube devices are 5% quantum efficient and solid state devices are 60% to 95% quantum efficient

## Slide 24: SMALL CAMERAS
Source: VISION SYSTEMS DESIGN, November 2010, “Color Camera Cubes”, p. 17

## Slide 25: Multispectral Sensor Chip
2.7×2.7×1.1 mm in size
Two versions: 1) 385-900 nm, 2) 775-1065 nm
Manufactured by Viavi Solutions
Development kit available
Photonics Spectra, June 2017, p. 36

## Slide 26: Imaging Outside the Visible Range of the EM Spectrum
Wavelength in nanometers

## Slide 27: X-Rays: Used in medical diagnostics and computerized tomography (CT)
Chest X-ray
Dental X-ray

## Slide 28
One slice of CT of patient’s abdomen
Computerized Tomography

## Slide 29
Ultraviolet imaging (300nm): Used in industrial applications, law enforcement, microscopy and astronomy
Fluorescence microscopy of cells
Fluorescence microscopy of cells

## Slide 30
Infrared imaging (800nm+): Used in satellite imaging, law enforcement, medical diagnosis and fire detection
Satellite image showing
water vapor
Infrared satellite imagery in the
near infrared band

## Slide 31
Infrared imaging (800nm+): Used in satellite imaging, law enforcement, medical diagnosis and fire detection
Thermographic images used in research for the diagnosis of Chiari malformation, a brain disease, in dogs

## Slide 32
Multispectral imaging: Used in weather analysis
GOES image of North America
(Multispectral Geostationary Operational Environment Satellite)

## Slide 33
Microwave images: Used in radar applications, to acquire info through obstacles in any light conditions
Radio waves: Used in astronomy and medicine (MRI)
MRI of patient’s shoulder

## Slide 34: Acoustic Imaging
Works by sending out sound waves at various frequencies and then measuring the reflected waves
Used in biological and man-made systems, geological systems, and medicine
Conventional ultrasound
3-D Ultrasound

## Slide 35: Electron Imaging
Uses a focused beam of electrons
Provides high magnification (200 thousand times)
Two types: SEM (scan) and TEM (xmit)
SEM image of mosquito
Logic gate in microchip
Brittlestar

## Slide 36: Laser Imaging
LASER = Light Amplification by Stimulated Emission of Radiation
Produces narrow beam of light in visible, IR, or UV range of EM spectrum
Generates coherent light, highly intense and monochromatic
Used to create range images, referred to as depth maps

## Slide 37: Computer Generated Images
Computers are used to generate images, they are not sensed from the real world
Used in engineering (CAD), medicine, education, arts, games, aviation

## Slide 38: The CVIPtools Software
Developed at SIUE
Provides the user access to a wide variety of computer imaging operations and to explore these operations by varying all the parameters and observing the results in real time
Continually under development in the university environment, so that newly developed algorithms are available for exploration and research

## Slide 39
Image Viewer
Loading an image requires clicking on the standard file open icon in the upper left of the main window
The image is read into the memory and its name appears in the image queue and is displayed in the main window
Image information shown in the status bar at the bottom of the main window

## Slide 40
The loaded image is the active image, which can be changed at anytime either by clicking on the image name in the queue or the image itself
The image viewer allows the user to perform standard image geometry as well as image enhancement operations via histogram equalization
These operations affect only the image that is displayed, and not the images in the CVIPtools image queue
Image Viewer

## Slide 41
Main Window with images in queue

## Slide 42: Viewer Commands

## Slide 43: Viewer Commands (cont’)

## Slide 44: Image Representation
Optical image: Collection of spatially distributed light energy measured by an image sensor to generate I(r,c)
Matrix: 2-D array corresponding to the image model, I(r,c)
Vector: One row or column in a matrix

## Slide 45: Image Types
Binary images: Simplest type of images, which can take two values, typically black or white, or “0” or “1”
Gray scale images: One-color or monochrome images that contain only brightness information and no color information
Color images: 3 band monochrome images, where each band corresponds to a different color, typically red, green and blue or RGB

## Slide 46
  Color pixel vector: Single pixel’s values for a color image, (R,G,B)
  Multispectral Images: Images of many bands, which may contain information outside of the visible spectrum

## Slide 47: Color Transform/Color Model
Mathematical model or algorithm to map RGB data into another color space
Decouples brightness and color information
Hue/Saturation/Lightness (HSL), Hue/Saturation/Value (HSV) and Hue/Saturation/Intensity (HSI) Color Transforms:
Describes colors in terms that we can more readily understand

## Slide 48
Hue corresponds to color, saturation corresponds to the amount of white in color, and lightness, intensity or value is the brightness
For example: a deep, bright orange color would have a large lightness/intensity/value (bright), a hue of “orange”, and a high value of saturation (“deep”)
But in terms of RGB components, this color would have the values as R=245, G=110, and B=20

## Slide 49: Creation of Orange Image in CVIPtools

## Slide 50: HSL Color Space

## Slide 51: RGB to HSL Mapping

## Slide 52
Equations for mapping RGB to HSI are:
Note: See text for HSL, HSV and inverse of the equations

## Slide 53
Spherical Coordinate Transform (SCT):
Maps color information into two angles (A and B),
and the brightness into color vector length (L)
Equations relating SCT to RGB components are:

## Slide 54: Spherical Coordinate Transform
Then SCT represents a color pixel vector by two angles and the vector length

## Slide 55
Cylindrical coordinate transform (CCT):
Does not completely separate brightness and color information
Application specific
Equations for finding CCT are:

## Slide 56
Cylindrical coordinates transform
Then CCT represents a color pixel vector by one angle and two distance measures
z = B

## Slide 57
Comparing colors in the previously defined color spaces are not well correlated to human visual perception
Color perception. Color A may be green and color B may be orange.
Colors C and D may be slightly different shades green, but ΔCD = ΔAB.

## Slide 58
Chromaticity coordinates:
Normalizes RGB values to the sum of all three
Chromaticity coordinates are:

## Slide 59
CMY (Cyan, Magenta, Yellow)/CMYK:
Color transform based on subtractive model
Used for color printing:
  C = 1- R; M = 1 – G ; Y = 1 – B; K = Black
PCT (Principal components transform):
Examines all RGB vectors within an image
Finds linear transform, that aligns the coordinate axes so that most of the information is along one axis, the principal axis

## Slide 60: Digital Image File Formats
Bitmap images (raster images): Images that can be represented by our image model, I(r,c)
Vector images: Artificially generated images by storing only mathematical description of geometric shapes using key points
Rendering: Process of turning a vector image into a bitmap image

## Slide 61
Image file header: A set of parameters found at the start of the file image and contains information regarding:
  Number of rows (height)
  Number of columns (width)
  Number of bands
  Number of bits per pixel (bpp)
  File type

## Slide 62
Look-up table (LUT): Used for storing RGB values for 8-bit color images

## Slide 63
Common image file formats are:
BIN, RAW
PPM,PBM,PGM
BMP
JPEG, JPEG2000
TIFF
GIF
RAS (Sun – old format)
SGI (Silicon Graphics – old format)
PNG
PICT (old Apple format)
EPS
VIP, VIPM

## Slide 64
Remapping for display. If data range exceeds the bounds of a standard 8-bit (per band) image, it must be remapped for display. Typically with a linear remapping process. Note that data precision will be lost.