## Slide 1
Mechanisms and Machines Kinematics, Dynamics, and Synthesis
Kinematic Analysis Part I:
Vector Loop Method
Chapter 2

## Slide 2: Student Objectives and Sections
Objectives:
  Introduce Vector Loop Method
  Assign vector loops to mechanism properly
  Use method to analyze one-degree-of-freedom mechanisms
Sections:
  2.1 Kinematic Analysis and the Vector Loop Method
  2.2 Hints for Choosing Vectors
  2.3 Closed-Form Solutions to the Position Equations
  2.4 Numerical Solutions to Position Equations
  2.5 The Motion of Points of Interest

## Slide 3: Kinematic Analysis of One-DOF Mechanisms
Consists of the following problem | 
You are given: | Dimensions of mechanism State of motion (position, velocity, acceleration) of one link (input)
You solve for: | State of motion (position, velocity, acceleration) of all other links and points of interest, like mass centers

## Slide 4: Why Vector Loop Method?
Beginning mechanics courses deal only with velocity and acceleration aspects of the problem, since position part is complex and non-linear
Vector Loop Method:
  Works with all three aspects of problem
  Is well suited to computerization

## Slide 5: 2.1 Kinematic Analysis and the Vector Loop Method
First task before applying Vector Loop Method is to correctly assign the vector loop
  This process is elaboration upon in 2.2
Vector loops lead to set of position equations that describe the changing configuration of the mechanism

## Slide 6: Steps in Vector Loop Method
Attach a vector to each link in mechanism, such that vectors form a closed loop
Write vector loop equation, i.e. the sum of the vectors in the loop is zero
Place origin of XY coordinate system at fixed point in vector loop
Decompose vector loop equation into X and Y components to produce position equations

## Slide 7: Steps in Vector Loop Method
List scalar knowns and unknowns
  If # of unknowns > # of equations → mechanism is movable
  If # of unknowns ≤ # of equations → not a mechanism; statically indeterminate
Solve for the position unknowns
Differentiate position equations to generate velocity equations and then solve for velocity unknowns
Differentiate velocity equations to generate acceleration equations and then solve for acceleration unknowns

## Slide 8: 2.2 Hints for Choosing Vectors
There are correct and incorrect ways of assigning vectors in mechanism
While choosing vectors, you can their verify correctness by:
  Checking that a known magnitude or direction of the vector corresponds to a dimension of the mechanism
  Checking that an unknown magnitude or direction corresponds to a joint variable or defines orientation of a link in the mechanism

## Slide 9: Evaluating Vector Loops
You can determine whether there are sufficient vector loops and whether good vectors have been selected by asking:
Does the # of unknown magnitudes and directions exceed the # of equations by the # of DOFs?
Do the known and unknown magnitudes and directions satisfy the vector checks on the previous slide?

## Slide 10: Vector Loop Assignment Examples
Straight Sliding Joint (2.2.1)

## Slide 11: Vector Loop Assignment Examples
Circular Sliding Joint (2.2.2)

## Slide 12: Vector Loop Assignment Examples
Externally Contacting Circular Bodies (2.2.5)

## Slide 13: 2.3 Closed-Form Solutions to Position Equations
Closed-Form means that unknowns can be calculated without iterative or numerical techniques
Closed-Form solutions are generally limited to systems of linear equations, while position equations are typically nonlinear (sine and cosine terms)
Some nonlinear systems have closed-form solutions, e.g. four bar or crank-slider mechanism

## Slide 14: 2.4 Numerical Solutions to Position Equations
Most mechanisms do not have closed-form solution
We will use Newton’s method to solve nonlinear position equations
Doing so converts the original system of nonlinear equations into a system of approximate linear equations

## Slide 15: Newton’s Method

## Slide 16: 2.5 The Motion of Points of Interest
Often analysis requires calculation of position, velocity, acceleration of a “point of interest” on a link
Examples of points of interest include:
  Mass centers, whose accelerations are used to estimate driving torques or bearing forces
  Points of application of driving or load force, which relate to mechanical advantage (Chapter 7)

## Slide 17: EXAMPLES
Mechanisms and Machines: Kinematics, Dynamics, and Synthesis Michael M. Stanišić

## Slide 18: Example 2.7

## Slide 19: Example 2.7

## Slide 20: Example 2.11